## Slide 1: We're Watching You: An analysis of IP cameras through their firmware
Charles Monett
OISF - November 2016

## Slide 2: Warning/Disclaimers
Please use this knowledge only for good and for your own devices.
Disclaimers:
All trademarks/etc. used in this presentation are property of their respective owners.
All testing performed in a controlled environment.

## Slide 3: Outline
Introduction/Key Points/Takeaways
Example 1: Conference Camera + demos
Example 2: Security Camera + demos
Some good news
Usage/Research
Wrap-up/Q&A

## Slide 4: Introduction
Did product research for IP cameras
  Was looking at more upmarket cameras (above Foscam)
  Part of it involved looking at firmware updates
  Was expecting a bit more resistance to modification
Not just tearing apart firmware
  Putting the knowledge to good use

## Slide 5: Key Points & Takeaways
Key points
  Network appliance design is hard to get right
  Sometimes we can use it for our advantage
Takeaways
  Introduction to tools/methods/processes
  Relevant applications that highlight security issues
  A greater understanding of IP cameras

## Slide 6: Example 1: Conference Camera
Vaddio ClearVIEW HD-USB Slotcard
Early-generation HD conference camera
Runs Ångström distribution of Linux
Powered by TI DaVinci DM368 platform
  (ARM926EJ-S CPU)
Provides HTTP/telnet/network streaming services

## Slide 7: Issues:
Network:
  Cleartext administration interfaces (HTTP/telnet), no alternatives
Firmware:
  Can be modified (in entirety) while running
  Firmware obfuscation is minimal (byte-reversal)
  Can be updated with modified firmware

## Slide 8: The update process
At System part of Administration menu:
User uploads firmware
Package is decoded and unpacked to scratch space.
Bootloader update script is executed
System update script is executed
System verifies functionality, and:
  If good, commits update.
  If not good, reverts to existing firmware.

## Slide 9: The firmware package
Relatively trivial unpacking. No binwalk needed.
A byte-reversed, base64 encoded zipfile containing:
  Bootloader
  Updated environment
  Support scripts
  Python Interpreter
  Other goodies

## Slide 10: Extracting & re-packing firmware
Extracting:
  Undo byte-reversal
  Uudecode file
  Extract resulting zip into a directory
Re-packing:
  Create zip archive
  Uuencode file
  Redo byte-reversal
If all goes well, it will accept your changes.

## Slide 11: Demonstration

## Slide 12: Example 2: Security Camera
Canon VB-H41
Pan/Tilt/Zoom IP camera
Proprietary OS (Linux-based)
Powered by DIGIC DV III Platform
  (ARMV6TEJ-based CPU)
SD slot for event recording

## Slide 13: Issues:
Network:
  None (if running as intended)
Firmware:
  Default administrative account is root
  Running software can be easily updated
  Arbitrary tasks can be invoked with cron job
  Easily unpacked, no apparent signature check in bootloader (?)
Enough space available to run Debian in a chroot.
  Remember that SD card slot?
  Applications only limited by binutils

## Slide 14: The firmware package
Courtesy of binwalk, we get the following:
128 bytes: Header (for this series)
Remainder is a tarred CPIO archive containing:
  Canon DryOS Bootloader (boot.bin)
  Data (cmr.dat)
  SquashFS filesystem (mtd4fs, ro) – core OS
  JFFS2 ‘appfs’ filesystem (main, mtd9fs, rw) – external apps
  Linux Kernel (zImage)
  MD5 sum of above items

## Slide 15: Extracting firmware
Extracting:
  Remove header
  Extract gunzip archive
  Extract resulting cpio archive in a directory
  Extract other filesystems
    SquashFS (core OS):
      unsquashfs mtd4fs.squashfs
    JFFS2:
      Extract/unpack to a loopback device
      Use Jefferson (jffs2 extraction tool)

## Slide 16: Demonstration

## Slide 17: Good News
VB-H41:
SSL is available (which raises the bar)
Some parts of firmware resist modification.
Some sanitization is performed (such as system logs)
HD-USB Slotcard:
Obtaining root is not straightforward
Outbound network traffic is restricted by default
Subsequent generation products more protected from altered firmware

## Slide 18: Usage
For good/neutral:
  Fix features (e.g. stepped Pan/Tilt)
  Extend functionality to cross-platform clients
  Ansible integration (depending on security model)
For [not good]:
  Unwanted surveillance
    Redirect/Copy streams to external sources
  Jumping-off point to other devices
    Other accounts (crafted alert e-mail)?
    Compromise other devices with the camera

## Slide 19: Further research
Obtain access without having to look over the wire
Extract keys from other devices (via JTAG, TTL serial, etc.)
Other firmware (Canon, AXIS, others)
Addressing issues with Canon firmware:
  Properly extracting squashfs
  Building firmware package (squashfs/jffs2-appfs)
NFS volume mounting off a camera (TI SDK kernel modules, perhaps?)
  Stream straight to networked storage.

## Slide 20: Questions?

## Slide 21: Resources:
Angstrom Distribution: http://www.angstrom-distribution.org/
Binwalk: http://www.binwalk.org/
SquashFS:
  http://tldp.org/HOWTO/SquashFS-HOWTO/mksqoverview.html
JFFS2 extraction:
  https://github.com/sviehb/jefferson
  http://linux-7110.sourceforge.net/howtos/netbook_new/x1125.htm
Multistrap: https://wiki.debian.org/Multistrap
TI DM365/368 SDK: http://www.ti.com/tool/linuxdvsdk-dm36x
Unpacking scripts: http://github.com/cm-code/firmware-scripts

## Slide 22: Thank you.