## Slide 1: Kali PoE
Dr. John W. Carls, CISSP, C|EH
Kali Linux on Raspberry Pi using Power over Ethernet

## Slide 2
Raspberry Pi
Kali Linux
Power over Ethernet
Demo

## Slide 3: Raspberry Pi - Raspberry Pi Foundation (https://www.raspberrypi.org/)
Raspberry Pi 3 Model B+
  Broadcom BCM2837B0 64-bit SoC
    Quad-core ARM Cortex-A53 1.4 GHz processor
    Dual Core VideoCore IV GPU (1 Gpixels/s ~ 2001 Xbox)
  1 GB LPDDR2 + microSD
  10/100/1000 Mbps Ethernet
  4 USB Ports
  Wireless ac/n + Bluetooth LE
  HDMI
Raspberry Pi 3 Model B
  Broadcom BCM2837 64-bit SoC
    Quad-core ARM Cortex-A53 1.2 GHz processor
  1 GB LPDDR2 + microSD
  10/100 Mbps Ethernet
  4 USB Ports
  Wireless n + Bluetooth LE
  HDMI
Raspberry Pi 2 Model B
  Broadcom BCM2836 32-bit SoC
    Quad-core ARM Cortex-A7 900 MHz processor
  1 GB + microSD
  10/100 Mbps Ethernet
  4 USB Ports
  Wireless
  HDMI
Raspberry Pi 1 Model B+
Raspberry Pi 1 Model A+
Raspberry Pi Zero W
  Wireless & Bluetooth
Raspberry Pi Zero

## Slide 4: Raspberry Pi - Raspberry Pi Foundation (https://www.raspberrypi.org/)
Raspberry Pi 4 Model B+
  Broadcom BCM2711 64-bit SoC
    Quad-core ARM Cortex-A72 1.5 GHz processor
    Dual Core VideoCore IV GPU (1 Gpixels/s ~ 2001 Xbox)
  1 / 2 / 4 GB LPDDR4-3200 SDRAM + microSD
  10/100/1000 Mbps Ethernet
  4 USB Ports (2 USB 3.0 / 2 USB 2.0)
  Wireless n / ac (2.4GHz / 5 GHz) + Bluetooth 5.0 LE
  Dual Micro-HDMI
  Power over Ethernet (PoE) enabled (requires PoE HAT)

## Slide 5: What is Kali Pi?
Combining Kali and Raspberry Pi
  Kali Pi
Kali Linux 2019.3
  Penetration Testing
    MetaPackages
Raspberry Pi
  Linux OS – Raspbian Linux (variant of Debian)

## Slide 6: Power over Ethernet (PoE)
Power over Ethernet or PoE describes any of several standard or ad-hoc systems which pass electric power along with data on twisted pair Ethernet cabling. This allows a single cable to provide both data connection and electric power to devices such as wireless access points, IP cameras, and VoIP phones.
There are several common techniques for transmitting power over Ethernet cabling. Three of them have been standardized by IEEE 802.3 since 2003. These standards are known as Alternative A, Alternative B, and 4PPoE. For 10BASE-T and 100BASE-TX, only two of the four signal pairs in typical Cat 5 cable are used.
Alternative B separates the data and the power conductors, making troubleshooting easier. It also makes full use of all four twisted pairs in a typical Cat 5 cable. The positive voltage runs along pins 4 and 5, and the negative along pins 7 and 8.
https://en.wikipedia.org/wiki/Power_over_Ethernet

## Slide 7: Power over Ethernet